## Slide 1
ALLEGRO IN-HAND ROTATION / TECHNICAL REPOSITORY COMPARISON
Isaac Lab migration with the HORA learning interface
The simulator, control plumbing and deployment ordering change; PPO and adaptation source files remain identical.
[1] isaaclab/allegro_hand_hora_env.py + wrapper.py [2] deploy_ros2*.py • Full paths and scope in speaker notes
01
ORIGINAL / ISAAC GYM
VecTask + gymtorch
Task + simulation loop
CURRENT / ISAAC LAB
DirectRLEnv + Articulation / RigidObject
Action / observation / reset hooks
HORA COMPATIBILITY WRAPPER
obs · priv_info · proprio_hist
terminated ∨ truncated → done
01 Policy contract
16 actions; 96-D observation
3 × [16 joint positions + 16 targets]
30 × 32 proprioceptive history
Stage 1 teacher → Stage 2 adaptation
02 Control semantics
120 Hz physics / 20 Hz policy
q* ← clip(q* + a / 24)
τ = clip(Kp(q* − q) − Kd q̇, ±0.5)
q̇ uses the previous physics state.
03 Deployment alignment
Finger-major ↔ joint-rank-major
4 × 4 transpose permutation aligns observations, history and actions.
Timeout flags retained for PPO.
Research implication: preserve the learning design while rebuilding simulation and hardware interfaces.
Notes: Comparison scope: local original /home/changsik/projects/inhand_manipulation/isaacgym_repo/allegro_inhand_rotation (HEAD 52d076c plus local edits to train_s1.sh and vis_s1.sh) versus /home/changsik/projects/inhand_manipulation/allegro_inhand_rotation (HEAD 79656ee plus all working-tree changes, including untracked export code), inspected 2026-09-21. This is an implementation comparison, not an experimental benchmark.
Source [1]: hora/tasks/isaaclab/allegro_hand_hora_env.py:284,703,726,761; hora/tasks/isaaclab/wrapper.py; configs/task/AllegroHandHora.yaml:9,20,39,98. Original: hora/tasks/base/vec_task.py and hora/tasks/allegro_hand_hora.py.
Byte comparison found hora/algo/ppo/*.py, hora/algo/padapt/*.py and hora/algo/models/*.py unchanged relative to the supplied original. Same source does not establish numerical or checkpoint equivalence across simulators.
The wrapper preserves time_outs separately from combined done flags. Observations contain normalized joint positions and joint targets, not measured joint velocities. The 30-step history is 30 x 32.
Control equation describes inherited incremental target / torque semantics ported to Isaac Lab; it is not proposed as a new controller. The new _apply_action stores previous joint positions to avoid a zero finite difference from lazy state reads.
Source [2]: hora/algo/deploy/deploy_ros2.py:63 and deploy_ros2_two_hands.py. The explicit self-inverse permutation is [0,4,8,12,1,5,9,13,2,6,10,14,3,7,11,15]. This aligns new simulation order with existing HORA/ROS mappings. No hardware validation was performed for this presentation.

## Slide 2
ALLEGRO IN-HAND ROTATION / TECHNICAL REPOSITORY COMPARISON
DIGIT sensing and mesh-object simulation
A left-hand DIGIT variant adds compliant contact surfaces, calibrated tactile rendering and mesh-object support.
[3] LeftAllegroHandDigitHora.yaml + allegro_hand_grasp_env.py [4] dataset_collection/sensors.py + object spawning
02
WHAT CHANGED RELATIVE TO THE ORIGINAL
HAND GEOMETRY
Standard HORA / V4 assets
→ Left DIGIT housings + 4 elastomer pads
GRASP DETECTION
CPU get_env_rigid_contacts
→ GPU ContactSensor per fingertip → object
OBJECT GEOMETRY
Primitive URDF objects
→ Native primitives + YCB / DexTouch meshes
Stable grasps: ≥2 contacts above 0.1 N,
plus proximity and height checks after warm-up.
TACTILE IMAGE GENERATION
01 Contact geometry
Rigid elastomer links use a compliant PhysX material.
02 Optical measurement
4 fingertip cameras + a pre-reset, no-contact baseline.
03 Tactile RGB + contact mask
Calibrated Taxim rendering via VisuoTactileSensor.
Contact pixel: d₀ − d > ε (default ε = 0.3 mm)
Notes: Source [3]: configs/task/LeftAllegroHandDigitHora.yaml and LeftAllegroHandDigitGrasp.yaml; assets/allegro/allegro_digit_left_elastomer.urdf. The original already supports standard left/right hands and ROS deployment; these are inherited features, not new contributions.
hora/tasks/isaaclab/allegro_hand_grasp_env.py:90-141 replaces the original CPU contact query with one object-filtered ContactSensor per fingertip. The code comments explain that combining multiple fingertip bodies into one filtered sensor produced zero forces in vectorized environments. After a 10-step warm-up, grasp validity requires all tips within 0.1 m of the object, at least two force magnitudes >0.1 N, and object height above threshold. Successful full episodes populate the grasp cache. GPU-compatible detection is a code capability; no throughput benchmark is claimed.
Source [4]: hora/tasks/isaaclab/allegro_hand_hora_env.py:102-184,314-323,563-685 for compliant materials and mesh spawning; scripts/dataset_collection/sensors.py:70-124,309-432 for calibrated DIGIT cameras and baseline capture. Primitive shapes use native Isaac Lab spawn configurations. Meshes use MeshConverter and cached USD with per-environment object/scale selection.
The elastomer is a rigid link with a compliant contact material, not a finite-element gel simulation. VisuoTactileSensor enables camera tactile output and disables force-field output. Calibration assets are required for Taxim rendering.
scripts/dataset_collection/neuralfeels_export.py:64 implements contact = finite(depth) AND depth>0 AND nominal-depth>mask_eps. Collector default mask_eps is 3e-4 m. No contact pixels are fabricated. Tactile sensing is added to dataset collection; the unchanged HORA policy remains proprioceptive rather than tactile-conditioned.

## Slide 3
ALLEGRO IN-HAND ROTATION / TECHNICAL REPOSITORY COMPARISON
From policy rollouts to NeuralFeels datasets
New Stage 1 and Stage 2 collectors export synchronized vision, touch, kinematics and object ground truth.
[5] collect_stage{1,2}_feelsight_dataset.py [6] dataset_collection/{neuralfeels_export,legacy_tactile,feelsight_writer,gt_sdf}.py
03
POLICY ROLLOUT
Teacher or adapted student
SYNCHRONIZED CAPTURE
4 DIGIT + scene RGB-D
FEELSIGHT EXPORT
Images + state + SDF
NEURALFEELS INPUT
Existing GT-depth loader
01 Frame consistency
Map joints by name; swap index / ring labels for NeuralFeels.
Tworld,cam = Tworld,tip · Ttip,cam
Every saved camera pose is checked against NeuralFeels FK.
02 Metric depth encoding
OpenGL camera axes; visible depth has negative camera-z.
z = uint8 / scale + offset
Fit scale / offset per episode; preserve masks with lossless storage.
03 Timing + ground truth
Render every physics step; exclude terminal auto-reset frames.
Save calibrated K, RGB-D, masks, hand / object poses and joint states.
Export object SDF at 0.5 mm pitch.
Research capability: calibrated tactile reconstruction datasets. Performance gains require experimental validation.
Notes: Source [5]: scripts/collect_stage1_feelsight_dataset.py:199,251,299-315 and scripts/collect_stage2_feelsight_dataset.py. Both collectors are new relative to the original repository. Rendering interval is set to 1. DirectRLEnv resets before returning done, so the terminal step is excluded to avoid mixing reset-state imagery into the prior episode. Nonempty short episodes are saved.
Source [6]: scripts/dataset_collection/neuralfeels_export.py, conventions.py, legacy_tactile.py, feelsight_writer.py, gt_sdf.py and README.md. The export targets existing NeuralFeels loaders in GT tactile-depth mode. Full end-to-end simulator/NeuralFeels execution was not performed for this presentation.
Export joint numbers: [8,9,10,11,4,5,6,7,0,1,2,3,12,13,14,15]. Index and ring sensor names are swapped. Actual sensor world camera matrices are compared with FK using np.allclose(atol=2e-5, rtol=0); this is a matrix-element tolerance, not an angular error bound. Camera offset relative to housing tip is (-0.002132,0.000021,0.017545) m with quaternion wxyz=(0.5,0.5,-0.5,-0.5).
Intrinsics come from actual sensors. Resizing uses fx'=sx*fx, fy'=sy*fy, cx'=(cx+0.5)*sx-0.5, cy'=(cy+0.5)*sy-0.5. Native tactile render is 640x480; default exported tactile image is 240x320 (W x H). Scene default is 640x480.
Tactile depth uses z=depth_uint8/digit_info.depth_scale + digit_info.cam_dist with zero reserved for no contact. The scale and offset are fitted to an episode to avoid saturation. Depth/mask names retain .jpg for existing loaders but payloads are lossless PNG; RGB uses JPEG. Scene metric depth is stored in depth.npz with scale 1. Object ground truth SDF default voxel pitch is 5e-4 m.
The new CPU regression suite tests compatibility against extracted original consumer source without optional SLAM imports; no test result is asserted in this deck. The scope includes current uncommitted/untracked edits as of 2026-09-21. There are no measured performance comparisons in this source review.